## Slide 1: Foundations of Switching and Multiplexing
Group Members:
Humna Imran (2023-BS-AI-017)
Maham Nisar (2023-BS-AI-058)
Ayesha Imran (2023-BS-AI-057)
Mukedas (2023-BS-AI-008)

## Slide 2: The Core Objective of Networking
unioffaisalabad
www.tuf.edu.pk
The Main Problem: We have limited physical wires and hardware, but millions of people want to talk at the same time.
Goal: To make sure data reaches the right person as cheaply and quickly as possible.
Simple Example: A highway is built once, but thousands of different cars share it to reach different cities.
The Solution: We cannot give every person their own private wire. Instead, we use Switching (to find a path) and Multiplexing (to share that path).

## Slide 3: What is Network Switching?
unioffaisalabad
www.tuf.edu.pk
Definition: It is the process of connecting different points (nodes) to create a temporary path for data.
How it works: A "Switch" acts like a smart controller. When it receives data, it looks at the destination address and "switches" the data to the correct output wire.
Key Concept: Switches make decisions based on a Forwarding Table (a map stored in their memory).

## Slide 4: Circuit Switching (The Dedicated Path)
unioffaisalabad
www.tuf.edu.pk
Definition: Before you send any data, a private and fixed physical path is reserved for you.
The 3 Steps:
  Setup: The network "books" the path from start to finish.
  Data Transfer: You send your data. No one else can use this path during your session.
  Teardown: The path is released so others can use it.
Main Benefit: Guaranteed speed with zero interruptions.
Real-life Example: Old-fashioned landline telephone calls.

## Slide 5: Switching Fabrics (Internal Design)
Space-Division Switching: Uses physical hardware "cross-points" to connect wires. It is fast but can become very expensive as the network grows.
Time-Division Switching: Uses memory called Time Slot Interchangers (TSI). It takes data from different users and changes their "time slots" to move them across the same wire.
Modern Systems: Most modern switches combine both (Multi-stage) to be both fast and cheap.
unioffaisalabad
www.tuf.edu.pk

## Slide 6: Message Switching (Store-and-Forward)
unioffaisalabad
www.tuf.edu.pk
Concept: The entire message is sent as one big block. It must be fully received and "stored" at a switch before it can be "forwarded" to the next one.
The Big Problems:
  Delay: You have to wait for the whole message to arrive at every stop.
  Storage: Switches need huge memory to hold big files.
  Errors: If there is a tiny mistake at the end of a big file, you have to resend everything.

## Slide 7: Packet Switching (Today's Standard)
unioffaisalabad
www.tuf.edu.pk
Definition: Data is broken into small "Packets." Each packet has a header (address) and can take its own rasta (path).
Why it is better:
Efficiency: Many people can send packets over the same wire at once.
Fault Tolerance: If one path is blocked, the packet can automatically find a new one.
Real-life Example: The Internet, Emails, and Video Streaming.

## Slide 8: What is Multiplexing?
unioffaisalabad
www.tuf.edu.pk
Definition: Combining many low-speed signals into one high-speed "super-pipe."
The Reason: Fiber optic cables are very powerful. Multiplexing allows us to pack thousands of conversations into one single cable.
The Tools:
MUX: Combines signals at the start.
DEMUX: Separates them at the end.

## Slide 9: Synchronous TDM (STDM)
unioffaisalabad
www.tuf.edu.pk
Mechanism: Time is divided into "slots." Every user is given a fixed slot in a fixed order (A, then B, then C).
No Address Needed: Since the order is fixed, the receiver knows that "Slot 1" is always from User A.
The Flaw (Waste): If User A is not talking, their slot still goes across the wire empty. This wastes the network's capacity.

## Slide 10: Statistical TDM (The Smart Way)
unioffaisalabad
www.tuf.edu.pk
Concept: Slots are not fixed. A slot is given only to a user who actually has data to send (On-demand).
The Rule: "First come, first served."
The Requirement: Because the order is not fixed, every piece of data must have an Address Header so the receiver knows who sent it.
Result: It is much more efficient than STDM because no slots are wasted.

## Slide 11: Statistical Multiplexing Gain (SMG)
Theory: It assumes that not everyone will use their full internet speed at the exact same time.
The Benefit: This allows Internet Providers (ISPs) to connect 100 people to a wire that technically only supports 50. This makes internet much cheaper for us.
Formula: $SMG = \frac{\text{Total User Speed}}{\text{Actual Link Speed}}$
Logic: Successful if SMG > 1.
unioffaisalabad
www.tuf.edu.pk

## Slide 12: Comparison & Conclusion
Circuit Switching: Best for voice calls because it is steady and reliable.
Packet Switching & ATDM: Best for the Internet because it is flexible and efficient.
Final Summary: Switching builds the "Bridge," and Multiplexing makes sure as many people as possible can cross it at once.
unioffaisalabad
www.tuf.edu.pk

## Slide 13: THANK YOU