## Slide 1
The philosophy and architecture of routing data through finite physical infrastructure, enabling infinite conversations to share limited resources.
Foundations & Circuit Switching
Name:
Humna Imran: 2023-BS-AI-017
Maham Nisar: 2023-BS-AI-058
Ayesha Imran: 2023-BS-AI-057
Mukedas: 2023-BS-AI-008
Notes: 1

## Slide 2
The Goal
Routing data and sharing finite physical infrastructure among infinite conversations.
Circuit Switching
Pre-allocates a dedicated, end-to-end path before sending data.
01
Setup
Reserves bandwidth and resources
02
Data Transfer
Continuous bit stream with guaranteed capacity
03
Teardown
Explicitly releases resources
Total Time Calculation: Transmission time (\frac{L}{R}) happens only once.
The Philosophy & Architecture of Circuit Switching
unioffaisalabad
www.tuf.edu.pk
Notes: 2

## Slide 3
Space-Division Switching
Uses physical paths such as crossbars and Clos Networks to create dedicated connections.
Time-Division Switching
Swaps time slots using memory through Time Slot Interchangers to share physical infrastructure.
Message Switching (The Precursor)
  Store-and-Forward: Entire message sent, stored at a node, then forwarded
  The Flaw: Requires massive buffers. One bit error means retransmitting the entire file
unioffaisalabad
www.tuf.edu.pk
Switching Fabrics & Message Switching
Notes: 3

## Slide 4
Circuit Switching
A single diagonal setup line, followed by a smooth, parallel transfer of data. Delay is purely propagation.
Message Switching
A "staircase" effect. Data stops entirely at each node to be stored before moving to the next, multiplying transmission delays.
unioffaisalabad
www.tuf.edu.pk
Timing Visual: Circuit vs. Message Switching
Notes: 4

## Slide 5
Messages are fragmented into smaller blocks (packets) with a header and payload.
Datagram Networks (e.g., IP)
  Connectionless
  Packets routed independently
  Arrive out-of-order
  Highly scalable and resilient to failures
Virtual Circuit (VC) Networks (e.g., ATM)
  Connection-oriented
  Setup creates a fixed logical path
  Packets arrive in order
  Physical wire is still shared dynamically
unioffaisalabad
www.tuf.edu.pk
Packet Switching (The Modern Standard)
Notes: 5

## Slide 6
Head-of-Line (HOL) Blocking
Occurs in input-queued switches. The first packet in line waits for a busy output, blocking all packets behind it (even if their outputs are free).
The Problem
HOL blocking reduces throughput to ~58%
The Solution
Virtual Output Queuing (VOQ)
The Result
Throughput boosted to nearly 100%
Virtual Output Queuing (VOQ): Input queues keep separate logical lines for each output port, eliminating HOL blocking.
unioffaisalabad
www.tuf.edu.pk
Inside the Router: Advanced Nuance
Notes: 6

## Slide 7
Feature
Circuit Switching
Datagram Packet
Dedicated Path
Yes
No
Yes (Logical)
Bandwidth
Reserved / Guaranteed
Dynamic / Best Effort
Reserved / Managed
Setup Phase
Required
None
Required
Header Size
None (after setup)
High (Full IP address)
Low (Short VC tag)
unioffaisalabad
www.tuf.edu.pk
Comparing Switching Paradigms
Virtual Circuit Packet
Notes: 7

## Slide 8
Goal: Multiple signals sharing a single physical wire/fiber.
Frequency Division Multiplexing (FDM)
Divides spectrum into frequency channels, separated by empty "guard bands" to stop interference.
Wavelength Division Multiplexing (WDM)
FDM for fiber optics. Multiple lasers shoot distinct colors (wavelengths) down one fiber.
unioffaisalabad
www.tuf.edu.pk
Multiplexing Foundations
Notes: 8

## Slide 9
Mechanism
Divides time into fixed frames and slots. Samples inputs in strict round-robin order.
Data Rate Calculation
Multiplexing N sources at R bps requires link capacity:
The Inefficiency
If a source is idle, its assigned time slot travels empty. Bandwidth is wasted.
unioffaisalabad
www.tuf.edu.pk
Synchronous Time Division Multiplexing (STDM)
Notes: 9

## Slide 10
Statistical TDM (ATDM)
Solves STDM's wasted space by allocating slots dynamically, strictly on demand.
The Trade-off
Every packet must carry an addressing header to identify the sender.
The Risk
Deep buffers are needed. If everyone transmits at once, queuing delays (jitter) occur.
unioffaisalabad
www.tuf.edu.pk
Statistical TDM & Expert Synthesis
Notes: 10

## Slide 11
Capitalizes on "bursty" traffic (users alternate between idle and downloading). Allows ISPs to oversubscribe links intentionally.
SMG = \frac{\sum_{i=1}^{N} R_{peak_i}}{C_{link}}
SMG > 1: Successful over subscription, relying on the statistical probability that not everyone transmits simultaneously.
unioffaisalabad
www.tuf.edu.pk
Statistical Multiplexing Gain (SMG)
Notes: 11

## Slide 12
Feature
Synchronous TDM (STDM)
Allocation
Fixed, round-robin
Dynamic, demand-driven
Overhead
None (position = ID)
Required in every slot
Efficiency
Low (wastes idle slots)
High (near 100% efficient)
Best For
Uncompressed Voice/Video
Bursty Data (Internet)
unioffaisalabad
www.tuf.edu.pk
STDM vs. Statistical TDM
Statistical TDM (ATDM)
Notes: 12